## Slide 1: SPP TCR Reference Price Calculation
A review of the SPP TCR Reference Price calculation and a proposal to modify the calculation to reduce over-collateralization
5/---/2017

## Slide 2: Motivation
Why over-collateralization is not good:
  Illiquid market
    Auction values are not reflective of actual market value, but may include the cost of posting such collateral
  Inefficiency
    Lack of counterflow bids may result in high clearing price on paths that affect binding constraints in the prevailing direction

## Slide 3: Principles
Comply with FERC Order 741
Principles:
  More credit requirements with Increasing volatility
  More credit requirements with Increasing bids
  For new nodes that lack historical data, credit calculation should use historical data of the closest nodes

## Slide 4: More credit requirements with Increasing volatility
Average
$/MWh Congestion Value
On two paths that have the same Monthly value, when they are bid at the same bid price, the more volatile path on the left will be assessed a higher credit requirement

## Slide 5: More credit requirements with Increasing bids
Average
$/MWh Congestion Value
When comparing two bids on the same path, the more expensive bids on the left will be assessed a higher credit requirement
Bid Price 1
Bid Price 2

## Slide 6: Current SPP Reference Price Calculation
How is TCR_REFERENCE_PRICE calculated?
Stress Test Price based on 90%-tile of the opposite value
TCR_REFERENCE_PRICE
Mean
ETCRE farther away from Mean even though the distribution of value is the same as previous

## Slide 7: Current SPP Reference Price Calculation Comparing Published v. Calculated Jun_17 OFF
Source | Sink | Reference Price in $/MWh
OKGECENTWIND | OKGESNRWIND | 31.28
OKGEKEENANWIND | CSWSLEEPINGBEAR | 24.91
OKGECENTWIND | WR.MW.GMEC.MW | 17.01
Downloaded Hourly Reference Price $/MWh
Calculated Reference Price $/MWh
Source | Sink | Reference Price in $/MWh
OKGESNRWIND | WR.MW.GMEC.MW | -43.24
INDN_MWE_SMKY2 | CSWMAJESTICWIND | -25.47
Source | Sink | Reference Price in $/MWh
SECI.FPLP.GRAYWIND | WAUE.BEPM.BRADY1 | 0
Calculation matches closely with the SPP published Reference Price

## Slide 8: Proposing a Reference Price Calculation
Reflects the “statistical” worst-case congestion value of a particular TCR path for a particular period.
Such that when the product is bid at a particular bid price, the credit requirement corresponds to the spread between the bid price and the “statistical” worst-case congestion value.

## Slide 9: Calculating Statistical Worst Case
Given a particular path, we can “simulate” a Monthly value as follows: (suppose there are 400 relevant hours in a given Month)
  Step 1: Formulate distribution of the hourly congestion values
  Step 2: Draw from the distribution until we collect 400 hourly samples
  Step 3: Sum the 400 hourly samples to produce one Monthly sample, repeat Step 2 and 3 to get the next sample until we reach N samples
Given the N Monthly samples, we can say what is the statistical worst-case
  5%-tile is generally used when identifying a statistical worst-case

## Slide 10: Example of Simulating Monthly Congestion
An example of a TCR Path in Jun_16 OFF OKGESNRWIND to OKGECENTWIND
June 2016 OFF
0% 5% 10% 25% 50% Mean
-127.10960 -72.34076 -60.62520 -45.39283 -31.41060 -32.20895
Frequency
Hourly Congestion $/MWh

## Slide 11: Example of Simulating Monthly Congestion
Generating one Monthly sample from sampling the hourly distribution independently

## Slide 12: Example of Simulating Monthly Congestion
Monthly Congestion $/MW
Frequency
Simulated of Monthly Value based on June 2016 OFF Hourly Samples
0% 5% 10% 25% 50% Mean
-14396.39 -13564.46 -13411.86 -13129.72 -12844.96 -12828.47

## Slide 13: Example of Simulating Monthly Congestion
Hourly Value:
Simulated Monthly Value:
Monthly Average ~= 400 * Hourly Average
June 2016 OFF
0% 5% 10% 25% 50% Mean
-127.10960 -72.34076 -60.62520 -45.39283 -31.41060 -32.20895
Simulated of Monthly Value based on June 2016 OFF Hourly Samples
0% 5% 10% 25% 50% Mean
-14396.39 -13564.46 -13411.86 -13129.72 -12844.96 -12828.47

## Slide 14: Example of Simulating Monthly Congestion
Hourly Value:
Simulated Monthly Value:
Monthly Average width = -12828 – (-13564) = 736
Hourly Average width = -32 – (-72) = 40.13181
The ratio is about ~20 = sqrt(400)
June 2016 OFF
0% 5% 10% 25% 50% Mean
-127.10960 -72.34076 -60.62520 -45.39283 -31.41060 -32.20895
Simulated of Monthly Value based on June 2016 OFF Hourly Samples
0% 5% 10% 25% 50% Mean
-14396.39 -13564.46 -13411.86 -13129.72 -12844.96 -12828.47

## Slide 15
Need comments about assessing whether such valuation is an overestimate if the hourly samples are actually correlating

## Slide 16: Central Limit Theorem
Losely: sum of N independent samples of any probability distribution will follow a normal distribution
We can estimate Worst-Case value:
Where Y is the Hourly values and H is the number of hours in a period

## Slide 17: Comparing Reference Price to Statistical Worst-Case Value
Source | Sink | Reference Price in $/MWh | 5%-tile | 2%-tile | 50%-tile
OKGECENTWIND | OKGESNRWIND | 31.28 | 30.53 | 30.53 | 32.17
OKGEKEENANWIND | CSWSLEEPINGBEAR | 24.91 | 24.35 | 24.35 | 25.65
OKGECENTWIND | WR.MW.GMEC.MW | 17.01 | 18.87 | 18.82 | 19.72
Downloaded Hourly Reference Price $/MWh
Calculated Statistical Worst-Case Value $/MWh
Source | Sink | Reference Price in $/MWh | 5%-tile | 2%-tile | 50%-tile
OKGESNRWIND | WR.MW.GMEC.MW | -43.24 | -13.40 | -14.10 | -12.34
INDN_MWE_SMKY2 | CSWMAJESTICWIND | -25.47 | -8.67 | -9.00 | -7.27
Showing Reference Price results in much higher credit requirements on paths that are generally negatively congested
50%-tile
5%-tile
2%-tile
Statistical Worst Case
Statistical Worst Case
Statistical Worst Case

## Slide 18: Credit Requirements Example
Reference price is used to offset the credit requirement such that the Credit Requirement

## Slide 19: Examples

## Slide 20: Backtesting Credit Requirements of PY2016 Auction
Current Ref Price and the X%-tile WorstCase value. (test against the 5%-tile, 2%tile, and 1%tile)

## Slide 21: Proposal #1
Replace current calculation of Reference Price with Statistical Worst-Case Value

## Slide 22
Credit calculation involving new nodes

## Slide 23: New Nodes
Currently Reference Price calculation for paths involving new nodes will use the MCC average across all SPP points
  But by definition, the MCC congestion pricing if weighted by load power withdrawal is equal to zero.
  If sink points in general have negative MCC (like in Sunflower, Nebraska, or Westar), then most likely any paths sourcing at new nodes will require credits
  If sink points in general have positive MCC (like in OKGE, EDE, or WFEC), then most likely any paths sourcing at new nodes will require credits
And what about when both Source and Sink are new nodes. For example the path SECI.FPLP.GRAYWIND to WAUE.BEPM.BRADY1?
  Currently Reference Price for such path is zero.

## Slide 24: Proposal #2
Reference price on paths involving New Nodes, SPP will use historical data of the physically closest nodes

## Slide 25: Contact
Justin Riddell
jriddell@teainc.org
Yohan Sutjandra
ysutjandra@teainc.org

## Slide 26
Appendix

## Slide 27: OKGECENTWIND to OKGESNRWIND
Reference Price is exactly at Mean Price of 31.28 $/MWh
Texas
Oklahoma
Map Source: YesEnergy
June 2016 OFF
5% 10% 25% 50%
0.00030 3.18864 13.48485 31.41060

## Slide 28: OKGESNRWIND to WR.MW.GMEC.MW
Reference Price is -43.24 $/MWh is further out compared to the 5% tile.
Map Source: YesEnergy
Oklahoma
Texas
Kansas
June 2016 OFF
5% 10% 25% 50%
-32.28321 -24.57508 -19.17780 -11.91885

## Slide 29: SECI.FPLP.GRAYWIND to WAUE.BEPM.BRADY1
Both nodes are new nodes, current SPP Reference Price calculation results in 0 $/MW, for both directions
Map Source: YesEnergy
January 2017 – April 2017 OFF
5% 10% 25% 50% Mean
-3.518920 -0.422220 0.820550 4.720600 6.193856